## Slide 1: CLIM Software Architecture
Module 3

## Slide 2: Module Objectives
  Introduce the Cluster I/O Module (CLIM)
  Describe the common components of the CLIM
  Describe the CLIM theory of operation
  Describe how the CLIM connects into the NonStop Server
  Describe the Cluster I/O Protocol (CIP) software components
Notes: <footer>
<header>
<date/time>

## Slide 3: Cluster I/O Modules (CLIMs)
P Switches
Storage
ServerNet X Fabric
Storage
CLIM
Storage
CLIM
IOAME
SWAN
IP
CLIM
IP
CLIM
Notes: <footer>
<header>
<date/time>
IP CLIMs are also referred to as Network CLIMs.

## Slide 4: CLIM Product Overview
The Cluster I/O Module (CLIM) is a new generation of NonStop Adapters
  HP ProLiant DL385 G5 rack mount server
    Quad core processor
    Debian Linux operating system
One 72GB system disk
DVD drive not installed
Notes:   The default configuration for an IP CLIM is one X and one Y ServerNet link.
  The HP ProLiant DL385 G2 uses a dual core processor.

## Slide 5: Theory of Operation
  Cluster I/O Protocol (CIP) Subsystem
    Provides a configuration and management interface for I/O
  Uses a Linux server as a front end
    Moves network stacks from the NonStop host to a Linux server
  Leverages the open source Linux environment
  Dual ServerNet fabrics connections
  Provides Ethernet or Storage interfaces
NonStop Server
Application
Socket Calls
CIP Subsystem
TCP Stack
CIP Software
Ethernet Links
ServerNet
CLIM
NonStop Server
Application
DP2
CIP Subsystem
Disk drivers
CIP Software
Storage Devices
ServerNet
CLIM

## Slide 6: NonStop Parallel TCP/IP Subsystems
QIO
WEB
TCP(6)SAM $ZTC0
TCPLIB
LAN Drivers, DIH
CPU 0
ServerNet
FESA
172.17.217.44
FESA
172.17.217.44
TCP(6)MAN $ZZTCP
TCP(6)MON $ZPTM0
QIO
WEB
TCP(6)SAM $ZTC0’
TCPLIB
LAN Drivers, DIH
TCP(6)MAN $ZZTCP’
TCP(6)MON $ZPTM1
EXPAND
data-out
data-in
ARP
open() close()
CPU 1
SCF
SCP $ZNET
ZTCP(6)SRL/ZTCP6DLL
data-in
Master
Notes: <footer>
<header>
<date/time>
  This illustration shows all the components of parallel library NonStop TCP/IP.
  The CIP Subsystem has evolved from this architecture.

## Slide 7: NonStop CIP Subsystems
QIO
WEB
PROVIDER $ZTC0
CIPLIB
kIT-API
CPU 0
ServerNet
IP CLIM
172.17.217.44
IP CLIM
172.17.217.44
CIPMAN $ZZCIP
CIPMON $ZCM00
QIO
WEB
PROVIDER $ZTC0’
CIPLIB
kIT-API
CIPMAN $ZZCIP’
CIPMON $ZCM01
EXPAND
data-in/out
open() close()
CPU 1
SCF
SCP $ZNET
ZCIPDLL
data-in
Notes: <footer>
<header>
<date/time>
  This illustration shows all the components of parallel library NonStop TCP/IP.
  The CIP Subsystem has evolved from this architecture.

## Slide 8: PROVIDER Object
  Defines a collection of Ethernet resources and associates them with a transport provider
    Associates an IP CLIM to a PROVIDER object
      Directs socket requests to a specific CLIM
    One provider per IP CLIM (default)
      One provider per two IP CLIMs in a failover configuration
    A Provider has a corresponding CIPSAM process which is used by applications to select the transport service provider
  Two type of PROVIDERs
    IPDATA PROVIDER
      Associate with all normal data interfaces on all CLIMs associated with this PROVIDER
    Maintenance PROVIDER
      Associate with a maintenance interface on a specific CLIM

## Slide 9: NonStop Operating System CIP Components
  CIPMAN – Manager process ($ZZCIP)
  CIPMON – Monitor process ($ZCMxx)
  CIPSAM – Socket provider process
  CSIF – Common Socket Interface
  ZCIPSCF – SCF product module for CIP subsystem
  ZCIPPTR – PTRACE product module for CIP
  ZCIPDLL – Shared run-time resource library
  ZCIPMDLL – Shared run-time library to support Measure for CIP subsystem
  kIT-API/SCS – Kernel module for RDMA operation and messages over ServerNet
  CLIMCMD – Wrapper for communicating with CLIM via maintenance LAN using the Secure Shell (SSH)
Notes: Subsystem Control Facility (SCF)

## Slide 10: CIP Software Architecture Overview (IP CLIM)
SCF
CIPSCF
FS
ITAPI
CLIMAGT
CIPSSRV
LINUX Sockets
Capella Driver
CLIM/Linux
CIPSREQ
K
-
ITAPI
TNET Services
QIO
CIPMAN
-
B
CIPMAN
-
P
Socket
Appl
FS
CSIF
CIPSAM
One per PROVIDER
IKE
SSH
CIPMONF
K
-
ITAPI
QIO
TNET Services
CIPMON
…
CIPMON0
One per CPU
SCF
CIPSCF
FS
TACL
CLIMCMD
eth0:0
Notes:   Internet key exchange (IKE) used with IPsec.
  Interconnect transport application programming interface (ITAPI).

## Slide 11: CIP Software Architecture Overview (Storage CLIM)
SCF
CIPSCF
FS
ITAPI
CLIMAGT
CIPSSRV
LINUX Device drivers
Capella Driver
CLIM/Linux
K
-
ITAPI
TNET Services
QIO
CIPMAN
-
B
CIPMAN
-
P
DP2
IKE
SSH
CIPMONF
K
-
ITAPI
QIO
TNET Services
CIPMON
…
CIPMON0
One per CPU
SCF
CIPSCF
FS
TACL
CLIMCMD
eth0:0
DISK Driver
Notes:   Internet key exchange (IKE) used with IPsec.
  Interconnect transport application programming interface (ITAPI).

## Slide 12: Software Component — CIPMAN
  One process pair per HP Integrity NonStop NS-2000 server ($ZZCIP)
    Implemented using C++
  Provide central management point for CIP subsystem
  Manage CIP subsystem configuration records
  Monitor connection between CLIM hardware and the ServerNet switch
  Provide high-level management of each CLIM (including failover)

## Slide 13: CIP Software Component – CIPMAN
SCF / OSM / SNMP
Configuration Data Base
CIPMON
Processes
CIPMAN
Process
CIPMAN
-
P
Process
SPI
EMS
CLIM Mgmt
(via CIPMON using QIO)
CIPMON Mgmt
(using QIO)
HP SIM / OpenView
Hardware
Access
CLIM
Discovery

## Slide 14: CIP Software Component — CIPMON
  Manages connections with CLIM
  One process per CPU ($ZCMxx)
  Handles management requests from CIPMAN
    Includes sending requests to the CLIM via CIPSREQ
  Provides a “call back” feature so that CIPSREQ can function in CIPMON’s context
  Provides support for processing TCP/IP data in CIPMON context, including socket migration and resource cleanup
  Proxy process for ZCIPDLL, ZCIPMDLL, and CLIM for generating EMS and writing the trace record

## Slide 15: CIP Software Component — CIPMON
CIP Mgmt Responses and asynchronous messages (QIO)
NSK Config Services
DSM_TRACE
QIO
CIPMAN Process Pair
EMS
Trace
CIP Mgmt Requests (Procedure Calls)
EMSSEND
QIO
CIPMON Process
CIPSREQ (k-ITAPI)
NonStop Configuration Services
CSIF (Client Process)
CIP Management Responses and Asynchronous Messages (QIO)
Configuration Database
Common Socket Interface

## Slide 16: CIP Software Component – CIPSAM
  CIP Socket Access Method (CIPSAM)
    Based on TCP6SAM
  A process pair that provides applications with a name for a socket transport service provider
    One process pair per each PROVIDER object
  File system sends an open request to CIPSAM for each socket open
    Provide indication that this is a CIP socket for mapping to use CIP CSIF
  Handles duplicate open requests, backup open requests, close requests, and closes any openers that reside on a down CPU
  Provides support for SUBNET (but not ROUTE) object by using the SPI interface (for compatibility with conventional TCP/IP)

## Slide 17: CIP Software Component
  ZCIPDLL
    Shared run-time resource library
    Loaded into each CPU by the monitor process (CSIF/CIPREQ)
  ZCIPMDLL
    Provide interfaces between Measure and CIP subsystem
    Help gather information about CIP subsystem that is used by Measure
      Measure call ZCIPMDLL to get latest CLIM configuration in the current CPU

## Slide 18: CIP Software — CLIM Components (1 of 2)
  Capella driver
    Initializes and drives the ServerNet PCI-e card
    Provides neighbor check between the CLIM and the ServerNet switch
  IT-API/SCS Driver
    Initializes and drives the ServerNet interface between the NonStop operating system and the CLIM
  CLIMMON
    Responsible for starting and monitoring all other processes on the CLIM which interact which the NonStop operating system

## Slide 19: CIP Software — CLIM Components (2 of 2)
  CLIMAGT
    Responsible for processing host management and status request
      Not involved in data transfer or socket operations
    Supports bring up/down interfaces as requested
    Monitors changes in interfaces status and configuration
      Forwards information to the NonStop operating system
      Forwards EVLOG events to the host as EMS log events
  CIPSSRV
    Responsible for TCP/IP offload
      Processes all host socket requests and performs them by using standard Linux socket API
    For every socket created on the host, CIPSSRV will create one or more Linux sockets to be used to emulate the host socket calls
    Can have more than one CIPSSRV per CLIM

## Slide 20: CIP Data Flow — CIP Versus TCP/IPv6
SLSA
DIH
APP
ZTCP6DLL
TCP6MON
ZTCP6DLL
TCP/IPv6
kIT-API
APP
ZCIPDLL
CIPMON
ZCIPDLL
CIP

## Slide 21: CLIM Software
  CLIM software install
    The CLIM DVD is shipped with a SUT
    Install the CLIM DVD on a NonStop system console
      Windows Installer
    OSM low-level link (LLL) used to update CLIM Software
      Select version
      Automatically installed and CLIM restarted
  CLIM logging
    CIP subsystem logs events to the Linux evlog
    evlog records are forwarded to EMS by the CLIMAGT

## Slide 22
Notes: <footer>
<header>
<date/time>