## Slide 1: Storage Cluster I/O Module (CLIM)
Module 5

## Slide 2: Module Objectives
  Introduce the Storage Cluster I/O Module (CLIM)
  Describe the hardware components of the Storage CLIM
  Describe the Storage CLIM theory of operation
  Describe how the Storage CLIM connects into the NonStop Multicore Architecture (NSMA)
  Describe the disk and tape hardware components
  Volume Level Encryption overview
Notes: <footer>
<header>
<date/time>

## Slide 3: Storage Cluster I/O Modules (CLIMs)
P Switches
Ethernet
Storage
SWAN
IOAME
ServerNet X Fabric
Storage CLIMs
IP
CLIM
IP
CLIM
Notes: <footer>
<header>
<date/time>

## Slide 4: Distributed Disk Processes
Disk processes for different volumes can be distributed to any processors for load balancing
DP2
DP2
DP2
DP2
Adapters

## Slide 5: Product Overview
The Storage CLIM is a new generation of I/O adapter module based on HP ServerNet technology
  HP ProLiant DL385 G5 rackmount server
    Quad core processor
    Debian Linux operating system
  HP StorageWorks, Serial Attached SCSI (SAS), and Fibre Channel (FC) host bus adapter (HBA)
  Redundant ServerNet 3 links
    Two X-fabric and Two Y-fabric links
One 72GB system disk
DVD drive not installed

## Slide 6: Hardware Overview
  ProLiant DL385 G5 rackmount server
    AMD Opteron, quad core, 2.18GHz processor
    4x1GB PC2-5300 DIMM
    Five PCIe slots
    Redundant power and cooling
  ServerNet 3 to PCI adapter
      Two X-fabric and two Y-fabric connections
  SAS PCI-e HBA (HP SC44Ge)
    One internal and one external connector
      Four SAS links per connector (port)
        3Gbps per link
  FC PCI-e HBA (HP FC1242SR)
    Dual-channel (4 Gbps per channel)
SNET Adapter
SC44Ge
FC1242SR
Notes:     Fault-tolerant configuration requires the use of two Storage CLIMs.

## Slide 7: Storage CLIM Rear View
  Slots 1 and 2 are empty in the base Storage CLIM configuration, but could contain a Fibre Channel Adapter or a SAS adapter
  The ServerNet Adapter (Dual Capella) is always installed in Slot 3
Power supplies
3
X4
3
X4
3
X8
4
X8
4
X16
4
133
5
X8
5
133
PCIe
MHz
MHz
PCIe
PCIe
PCI-X
2
X4
PCIe
PCIe
1
X4
UID
2
1
iLO2
SAS HBAs
ServerNet Adapter
OSM Mgmt Interface port (ETH0)
ILO
Slot 1
Slot 2
Slot 5
Slot 4
Slot 3
Port not used on the Storage CLIM

## Slide 8: Theory of Operation
  Provides dual ServerNet fabric connections
  Provides Serial Attached SCSI (SAS) interface for a new generation of SAS storage subsystem and devices
  Provide Fibre Channel (FC) interface for Enterprise Storage Server (ESS) and FC tape devices
  Provides enclosure Environmental Monitoring Services
  Provides dual SAS domains from Storage CLIMs to dual-port SAS disk drives

## Slide 9: Storage CLIM Overview
  Supports Serial Attached SCSI and Fibre Channel
    HP StorageWorks MSA70 disk enclosure (up to twenty-five 2.5-inch SAS disks)
    HP XP Enterprise Storage Array (NED 1K, 10K, 20K models)
    Tape and virtual tape
  Can replace the I/O adapter module enclosure (IOAME) + Fibre Channel ServerNet adapter (FCSA) + Fibre Channel disk module (FCDM)
  ProLiant server running Debian Linux
    Uses Linux device drivers to transfer data to storage devices
$SYSTEM
$OSS
$AUDIT
$DSMSCM
Notes: <footer>
<header>
<date/time>

## Slide 10: Storage CLIM — Hardware Overview
StorageWorks MSA70 disk enclosure
  Twenty-five 2.5-inch disk drive slots
    72GB, 15K RPM
    146 GB, 15K RPM
    300GB, 10K RPM
  Two independent domains
    SAS Domain A
    SAS Domain B
  Two fans
  Two power supplies
  Fault-tolerant configuration requires the use of two StorageWorks MSA70 disk enclosures
MSA70 Rear View
Power Supply
Fan
I/O Modules
Module ID
Number

## Slide 11: Configurations
2c2d Configuration (Two controllers/two disks)
Two more MSA70s can be daisy-chained for a 2c4d configuration
4c4d Configuration
An 8c8d configuration is also supported
A Fault tolerant configuration with high availability

## Slide 12: Configuration – 2C2D
3
X4
3
X4
3
X8
4
X8
4
X16
4
133
5
X8
5
133
PCIe
MHz
MHz
PCIe
PCIe
PCI-X
2
X4
PCIe
PCIe
1
X4
UID
2
1
iLO2
3
X4
3
X4
3
X8
4
X8
4
X16
4
133
5
X8
5
133
PCIe
MHz
MHz
PCIe
PCIe
PCI-X
2
X4
PCIe
PCIe
1
X4
UID
2
1
iLO2
SAS Disk Enclosure 1
SAS Disk Enclosure 2
Storage CLIM 1
Storage CLIM 2
ServerNet adapter (slot 3)
SAS HBA (slot 5)
SAS HBA (slot 4)
Minimal fault tolerant configuration
Primary
Mirror Backup
Backup
Mirror
A B

## Slide 13: Configuration – 4C4D
3
X4
3
X4
3
X8
4
X8
4
X16
4
133
5
X8
5
133
PCIe
MHz
MHz
PCIe
PCIe
PCI-X
2
X4
PCIe
PCIe
1
X4
UID
2
1
iLO2
3
X4
3
X4
3
X8
4
X8
4
X16
4
133
5
X8
5
133
PCIe
MHz
MHz
PCIe
PCIe
PCI-X
2
X4
PCIe
PCIe
1
X4
UID
2
1
iLO2
3
X4
3
X4
3
X8
4
X8
4
X16
4
133
5
X8
5
133
PCIe
MHz
MHz
PCIe
PCIe
PCI-X
2
X4
PCIe
PCIe
1
X4
UID
2
1
iLO2
3
X4
3
X4
3
X8
4
X8
4
X16
4
133
5
X8
5
133
PCIe
MHz
MHz
PCIe
PCIe
PCI-X
2
X4
PCIe
PCIe
1
X4
UID
2
1
iLO2
Disk Enclosure 1
Disk Enclosure 2
Disk Enclosure 3
Disk Enclosure 4
Storage CLIM 1
Storage CLIM 2
Storage CLIM 3
Storage CLIM 4
Primary 1
Primary 2
Backup 1
Backup 2
Mirror 1
Mirror 2
Mirror Backup1
Mirror Backup1

## Slide 14: Daisy-Chaining SAS Enclosures
A maximum of four SAS disk enclosures can be daisy-chained together
3
X4
3
X4
3
X8
4
X8
4
X16
4
133
5
X8
5
133
PCIe
MHz
MHz
PCIe
PCIe
PCI-X
2
X4
PCIe
PCIe
1
X4
UID
2
1
iLO2
3
X4
3
X4
3
X8
4
X8
4
X16
4
133
5
X8
5
133
PCIe
MHz
MHz
PCIe
PCIe
PCI-X
2
X4
PCIe
PCIe
1
X4
UID
2
1
iLO2
Storage CLIM 1
Storage CLIM 2

## Slide 15: Storage CLIM — Supported Devices
StorageWorks MSA70: SAS disk enclosure
XP Enterprise Storage Array
FC Tape
SAS
Fibre Channel
SAS Tape
Notes: <footer>
<header>
<date/time>

## Slide 16: Storage CLIM — Recommended FRUs
FRUs | Online Replaceable? | Hot-Pluggable?
Microprocessor | No | No
Memory | No | No
Power supply | Yes | Yes
Fan | Yes | Yes
PCI-e Riser | No | No
SAS HBA | No | No
FC HBA | No | No
ServerNet adapter | No | No
Debian OS disk | No | Yes

## Slide 17: StorageWorks MSA70 — Recommended FRUs
FRUs | Online Replaceable? | Hot-Pluggable?
SAS disk drive | Yes | Yes
I/O module | Yes | Yes
Power supply | Yes | Yes
Fan | Yes | Yes

## Slide 18: Comparing FC to SAS Disk Drives
 | FC disks | SAS disks
Form factor | 3.5 inch | 2.5 inch
Capacity and spindle speed | 36GB/15k rpm 72GB/15k rpm 146GB/15k rpm 300GB/15k rpm | 72GB/15k rpm 146GB/10k rpm
Interface and speed | Fibre Channel, 2Gbps | SAS, 3Gbps
Number of channel/port | 2 | 2
Performance - Single track seek - Average seek - Full stroke seek | 0.57 ms 3.5 ms 9.0 ms | 0.2 ms 2.8 ms 5.1 ms

## Slide 19: Multiple Mirrored Volumes — Sequential I/O Operations
0
100
200
300
400
500
600
700
800
900
1000
Performance Example
Throughput (MB /Second)
Fiber Channel
353.0
265.0
G5 SAS (default)
738.0
641.0
G5 SAS (WCE)
737.4
738.0
Speedup G5 WCE vs Default
1.00
1.15
Sequential Read 56k
Sequential Write 56k
Notes:   Write cache enabled (WCE)
  A UPS is highly recommended if using the WCE setting.

## Slide 20: Multiple Mirrored Volumes — Random I/O Operations
0
2000
4000
6000
8000
10000
12000
14000
Performance Example
Throughput (I/O per second)
FiberChannel
6611
6284
G5 SAS (default)
12347
10788
G5 SAS (WCE)
12292
13964
Speedup G5 WCE vs Default
1.00
1.29
Random Read 4k
Random Write 4k

## Slide 21: Sequential Read Performance per CLIM
MB/s

## Slide 22: Rackmount Tape Drive Enclosure
Features
  HP StorageWorks products
  1U height
  Support up to two tape drives
  Two SAS connectors
  One power supply

## Slide 23: Tape Drives
Ultrium 448 SAS
Ultrium 920 SAS
 | Ultrium 448 SAS | Ultrium 920 SAS
Recording technology | LTO 2 | LTO 3
Compressed capacity (2:1) | 400 GB | 800 GB
Sustained xfer rate (compressed 2:1) | 173 GB/hr | 432 GB/hr
Encryption | No | No
WORM | No | Yes

## Slide 24: Product: Integrated Volume Level Encryption Through the Storage CLIM
Provides a system integrated volume level encryption solution for the NonStop
This is strictly a data at rest security solution
Encrypts all the data being written to configured disks and tape drives* attached to the NonStop Storage CLIM
* Full list of VLE compatible devices available in following slides
<number>

## Slide 25: System Interconnect
<number>
Sept 28, 2009
NonStop Volume Level Encryption FCS TOI. HP confidential - Need to know only
NonStop
Processors
ServerNet
Enterprise LAN
Maintenance LAN
Network CLIM
Network Adapter
NSC
CPU
CPU
CLIM
CLIM
ESKM
ESKM
Notes: <footer>
<header>
<date/time>

## Slide 26: Volume Level Encryption ESKM connection to NonStop
<number>
The recommended configuration includes having the customer use redundant network switches to configure the ESKM-CLIM network.
If a network switch fails in this configuration, half the CLIMs will still have access to the ESKM and as such any disk can still perform key rotation operations.
Notes: <footer>
<header>
<date/time>

## Slide 27: What is data at rest?
Data at rest is a term that refers to all data in computer storage while excluding data that is traversing a network (in motion) or data that is residing in computer memory to be read or updated (in use).
In Integrity NonStop context, that means data stored in our SAS disks, LTO-4 Tapes, XP arrays.

## Slide 28: Data At Rest Security NonStop VLE Overview – architecture view
Storage CLIM
<number>
SAS
HP StorageWorks
XP Arrays
LTO-4
H-series Systems
or
J-series Systems
Storage CLIM
    The HP Enterprise Secure Key Manager provides a high availability solution for managing and storing encryption keys.
HP Enterprise Secure Key Manager Cluster
Notes: <footer>
<header>
<date/time>

## Slide 29
<number>
July 28, 2026
FIPS = Federal Information Processing Standards
HP Enterprise Secure Key Manager
Key Management for NonStop VLE
Secure, centralized encryption key management
  Automates key generation, protection, and management based on security policies
  Supports unified key management across diverse products/applications
Strong auditable security, keys always encrypted at rest and in motion
  Hardened server appliance with FIPS 140-2 Level 2 validation pending
  Identity-based access, secure administration, logging, secure connection to Clients
Reliable lifetime key archival
  Automatic multi-site key replication, high availability clustering, and failover
  Supports 2-6 (or more) nodes, hundreds of clients, and millions of keys
The right encryption key, to the right device, at the right time
<number>
Notes: <footer>
<header>
<date/time>

## Slide 30
Notes: <footer>
<header>
<date/time>