## Slide 1: Common CLIM commands
Module 7

## Slide 2: Module Objectives
  SCF commands for CIP subsystem
  CLIM backup and CLIM restore
  climcmd
Notes: <footer>
<header>
<date/time>

## Slide 3: CLIM NonStop configuration
  Configure and start CIPMAN and CIPMON processes via SCF ADD PROCESS and SCF START PROCESS commands
  Configure and start CLIM via SCF ADD CLIM and SCF START CLIM commands, or OSM Service Connection Configure CLIM and Start actions
  Configure and start PROVIDER via SCF ADD PROVIDER and SCF START PROVIDER commands (for IP CLIM only)
  Configure and start attached disks and tapes via SCF ADD DISK, SCF ADD TAPE, SCF START DISK, and SCF START TAPE commands (for storage CLIM only)
  For enabling CLIMCMD commands a trusted partnership must be setup between the NonStop system and the CLIM. The SSOCLIM command must be used (from TACL) on the NonStop system to do that.
  All the steps should be already done for newly shipped systems or only the first one as part of DSM/SCM installation (adding CLIMS to NS16x00).

## Slide 4: SCF CIP Subsystem command matrix
|----------------------------------------------------------------------------|
| | A | A | A | D | I | L | N | P | S | S | S | S | S | T | V |
| | B | D | L | E | N | I | A | R | T | T | T | T | W | R | E |
| Commands | O | D | T | L | F | S | M | I | A | A | A | O | I | A | R |
| | R | | E | E | O | T | E | M | R | T | T | P | T | C | S |
| | T | | R | T | | O | S | A | T | S | U | | C | E | I |
| | | | | E | | P | | R | | | S | | H | | O |
| Object | | | | | | E | | Y | | | | | | | N |
| Type | | | | | | N | | | | | | | | | |
| | | | | | | S | | | | | | | | | |
|----------------|---|---|---|---|---|---|---|---|---|---|---|---|---|---|---|
| CLIM | x | x | | x | x | | x | | x | x | x | x | x | x | x |
|----------------|---|---|---|---|---|---|---|---|---|---|---|---|---|---|---|
| MON | x | | | | | x | x | | | x | x | x | | x | x |
|(CIPMON PROCESS)| | | | | | | | | | | | | | | |
|----------------|---|---|---|---|---|---|---|---|---|---|---|---|---|---|---|
| PROCESS | x | | | | x | | x | x | x | | x | x | | x | x |
|(CIPMAN PROCESS)| | | | | | | | | | | | | | | |
|----------------|---|---|---|---|---|---|---|---|---|---|---|---|---|---|---|
| PROVIDER | x | x | x | x | x | x | x | | x | | x | x | | x | |
|----------------|---|---|---|---|---|---|---|---|---|---|---|---|---|---|---|
| PROCESS | x | | | | x | | | x | | | | x | | x | x |
|(CIPSAM PROCESS)| | | | | | | | | | | | | | | |
|----------------|---|---|---|---|---|---|---|---|---|---|---|---|---|---|---|
| ROUTE | | x | | x | x | | x | | | | | | | | |
|----------------------------------------------------------------------------|
NOTE: 1. Object type NULL for VERSION and NAMES.

## Slide 5: SCF Info Provider
10-> info provider $zzcip.*
CIP Info PROVIDER
Name *TPName TYPE *HOSTNAME
ZTC0 $ZTC0 IPDATA DAGGER ZTCP0 $ZTCP0 MAINTENANCE osmlanx ZTCP1 $ZTCP1 MAINTENANCE osmlany
11-> info provider $zzcip.* ,detail
*TPName.................... $ZTC0 Type...................... IPDATA *HostID.................... 0.0.0.0 *Hostname.................. DAGGER *TCP-Listen-Que-Min........ 128 *BRecvPort................. No Ports Specified *Family.................... INET *Share-Ports............... 1000 Associated CLIMs:
Name Index N1002581 0 N1002583 1

## Slide 6: Cluster I/O Protocols (CIP)
$ZZCIP 9-> listdev tcpip
LDev Name PPID BPID Type RSize Pri Program
209 $ZTCP0 0,359 1,355 (48,0 ) 57344 201 \SABER.$SYSTEM.SYS04.CIPSAM
224 $ZTCP1 1,352 0,384 (48,0 ) 57344 201 \SABER.$SYSTEM.SYS04.CIPSAM
227 $ZTC0 0,387 1,367 (48,0 ) 57344 201 \SABER.$SYSTEM.SYS04.CIPSAM
$ZZCIP 10-> listdev cip
LDev Name PPID BPID Type RSize Pri Program
88 $ZZCIP 0,332 1,311 (74,0 ) 132 200 \SABER.$SYSTEM.SYS04.CIPMAN
182 $ZCM03 3,327 (74,1 ) 57344 200 \SABER.$SYSTEM.SYS04.CIPMON
183 $ZCM02 2,320 (74,1 ) 57344 200 \SABER.$SYSTEM.SYS04.CIPMON
184 $ZCM01 1,341 (74,1 ) 57344 200 \SABER.$SYSTEM.SYS04.CIPMON
185 $ZCM00 0,335 (74,1 ) 57344 200 \SABER.$SYSTEM.SYS04.CIPMON
Notes: $ZZCIP — Cluster I/O Protocol (CIP) manager
$ZCM## — CIP monitor

## Slide 7: List Devices
$ZZCIP 13-> listdev $zzcip
LDev Name PPID BPID Type RSize Pri Program
88 $ZZCIP 0,332 1,311 (74,0 ) 132 200 \SABER.$SYSTEM.SYS04.CIPMAN
$ZZCIP 14-> names $zzcip
CIP Names PROCESS \SABER.$ZZCIP
PROCESS
$ZZCIP
MON
$ZZCIP.ZCM00 $ZZCIP.ZCM01 $ZZCIP.ZCM02 $ZZCIP.ZCM03
PROVIDER
$ZZCIP.ZTC0 $ZZCIP.ZTCP0 $ZZCIP.ZTCP1
CLIM
$ZZCIP.S1002531 $ZZCIP.S1002533 $ZZCIP.N1002581 $ZZCIP.N1002583
Notes: The NAMES command returns a list of the object names and types subordinate to the
specified object.

## Slide 8: Cluster I/O Protocols — SCF Listopens (Mon)
$ZZCIP 15-> listopens mon $zzcip.zcm00
CIP Listopens MON \SABER.$ZZCIP.ZCM00
Openers Ppid State Proto Lport Provider CLIM
\SABER.$ZTN0 0,388 LISTEN TCP telnet ZTC0 *mult*
\SABER.$ZPR0 0, 23 LISTEN TCP 1089 ZTC0 *mult*
\SABER.$ZPR0 0, 23 LISTEN TCP echo ZTC0 *mult*
\SABER.$ZPR0 0, 23 LISTEN TCP finger ZTC0 *mult*
\SABER.$ZPR0 0, 23 LISTEN TCP ftp ZTC0 *mult*
CIP Listopens MON \SABER.$ZZCIP.ZCM00
Openers Ppid State Proto Lport Provider CLIM
\SABER.$ZPRP0 0, 19 LISTEN TCP 1089 ZTCP0 N1002581
\SABER.$ZTNP0 0,361 LISTEN TCP telnet ZTCP0 N1002581
\SABER.$ZPRP0 0, 19 LISTEN TCP echo ZTCP0 N1002581
\SABER.$ZPRP0 0, 19 LISTEN TCP finger ZTCP0 N1002581
\SABER.$ZPRP0 0, 19 LISTEN TCP ftp ZTCP0 N1002581
\SABER.$ZTNP0 0,361 ESTAB TCP telnet ZTCP0 N1002581
\SABER.$ZSSP0 0,407 LISTEN TCP 22 ZTCP0 N1002581
Notes: The LISTOPENS MON command displays a list of all sockets opened by processes in the processor containing the specified CIPMON.

## Slide 9: Cluster I/O Protocols — SCF Listopens (Provider)
$ZZCIP 16-> listopens provider $zzcip.ztcp1
CIP Listopens PROVIDER \SABER.$ZZCIP.ZTCP1
Openers Ppid State Proto Lport Provider CLIM
\SABER.$ZPRP1 1, 17 LISTEN TCP 1089 ZTCP1 N1002583
\SABER.$ZTNP1 1,354 LISTEN TCP telnet ZTCP1 N1002583
\SABER.$ZPRP1 1, 17 LISTEN TCP echo ZTCP1 N1002583
\SABER.$ZPRP1 1, 17 LISTEN TCP finger ZTCP1 N1002583
\SABER.$ZPRP1 1, 17 LISTEN TCP ftp ZTCP1 N1002583
\SABER.$ZSSP1 1,394 LISTEN TCP 22 ZTCP1 N1002583
CIP Listopens PROVIDER \SABER.$ZZCIP.ZTCP1
Openers Ppid State Proto Lport Provider CLIM
\SABER.$ZOSM 2,376 LISTEN TCP 9990 ZTCP1 N1002583
\SABER.$ZOEV 2,379 LISTEN TCP 9991 ZTCP1 N1002583
\SABER.$ZTMUX 2,380 0x00180 UDP 162 ZTCP1 N1002583
\SABER.$ZCMOM 2,377 LISTEN TCP 5989 ZTCP1 N1002583
Notes: The LISTOPENS PROVIDER command displays all sockets using the specified PROVIDER and
identifies the process that opened each socket.

## Slide 10: SCF Stats Mon
16-> stats mon $zzcip.ZCM00
CIP Stats MON \DAGGER.$ZZCIP.ZCM00
Sample Time ... 11 Dec 2008, 12:56:15.829
Reset Time .... 08 Dec 2008, 13:03:36.726SOCKET STATS
Total Recv Socket Reqs...... 575
Total Recv Errors........... 2
Total Send Socket Reqs...... 67609
Total Send Errors........... 0
Data Bytes Sent............. 50465612
Data Bytes Received......... 6978
Total Connections Out....... 26 Total Connections In........ 8
Current TCP Listen Sockets.. 10 High TCP Listen Sockets..... 10
Current UDP Sockets......... 3 High UDP Sockets............ 3
Current TCP Connections..... 2 High TCP Connections........ 4
Notes: <SCF> stats mon $zzcp.zcm00 (continued)
SOCKET SEND SIZE HISTOGRAM
Size 1-128.................. 37362 Size 129-256................ 34
Size 257-512................ 0 Size 513-1024............... 0
Size 1025-2048.............. 30213 Size 2049-4096.............. 0
Size 4097-8192.............. 0 Size 8193-12288............. 0
Size 12289-16384............ 0 Size 16385-32768............ 0
Size 32769 and larger....... 0
MON STATS
Total Messages Sent......... 67818
Total Messages Received..... 1607
Current Connected CLIMs..... 4 High Connected CLIMs........ 4
Total Rejected Connections.. 0 Deferred Sends.............. 0

## Slide 11: SCF Stats CLIM
17-> stats clim $zzcip.s1002531
CIP Stats CLIM \DAGGER.$ZZCIP.S1002531
Sample Time ... 11 Dec 2008, 13:04:26.000 Reset Time .... 08 Dec 2008, 13:03:40.000 CLIMMON STATS Event Log Entries......... 0 Restarts.................. 1 CLIMAGT Failures.......... 0 CIPSSRV0 Failures......... 0
CLIMAGT STATS
Event Log Entries........... 1 Buffer denials.............. 0 IT-API errors............... 0 Last IT-API error code...... 0 Linux errors................ 0 Last Linux errno............ 0 Current bfr bytes in use.... 160 High bfr bytes in use....... 4200 Total msgs sent............. 205662 Total msgs received......... 205660 Current connected Cpus...... 4 High connected Cpus......... 4 Queued Commands............. 1 Failed Commands............. 0
Notes: SCF> stats clim $zzcip.s1002531 (continued)
CIPSSRV0 STATS
Event Log Entries........... 0
Buffer denials.............. 0
IT-API errors............... 0
Last IT-API error code...... 0
Linux errors................ 0
Last Linux errno............ 0
Current bfr bytes in use.... 0
High bfr bytes in use....... 0
Total msgs sent............. 0
Total msgs received......... 0
Total bytes sent............ 0
Total bytes received........ 0
Current connected Cpus...... 0 High connected Cpus......... 0
Deferred Sends.............. 0 Failed Commands............. 0
Current TCP Listen Sockets.. 0 High TCP Listen Sockets..... 0
Current UDP Sockets......... 0 High UDP Sockets............ 0
Current TCP Connections..... 0 High TCP Connections........ 0

## Slide 12: SCF Switch CLIM
Example:
  switch clim $zzsto.S100271, away
    Same as “switch adapter $zzsto.<adapter name>” but for CLIMS
    Informs the NonStop system not to use a Storage CLIM

## Slide 13: Linux Events (1 of 2)
Linux events are automatically forwarded to EMS
  Sample Linux CLIM event
  00226 2008-01-29 15:15:31 \POS27.$ZCM00 TANDEM.CIP.H01 005227 CLIM Event CLIM Name: C100271 Logged by CLIM at: Tue Jan 29 15:15:04 2008 logger: 2008/01/29 23:15:04.000000 lunmgr: Do_update ().

## Slide 14: Linux Events (2 of 2)
SAS Disk Removal events
  00226 2008-01-29 15:15:31 \POS27.$ZCM00 TANDEM.CIP.H01 005227 CLIM Event CLIM Name: C100271 Logged by CLIM at: Tue Jan 29 15:15:04 2008 logger: 2008/01/29 23:15:04.000000 lunmgr: Do_update ().
  00227 2008-01-29 15:15:31 \POS27.$ZCM00 TANDEM.CIP.H01 005227 CLIM Event CLIM Name: C100271 Logged by CLIM at: Tue Jan 29 15:15:06 2008 kernel: 2008/01/29 23:15:06.909064 stomod: ctd: Table entry 003 disabled - lun = 102, id = 515
  00228 2008-01-29 15:15:31 \POS27.$ZCM00 TANDEM.CIP.H01 005227 CLIM Event CLIM Name: C100271 Logged by CLIM at: Tue Jan 29 15:15:06 2008 kernel: target0:0:2: delete device: fw_channel 0, fw_id 36, phy 1, sas_addr 0x5000c50000f7c481
  00229 2008-01-29 15:15:31 \POS27.$ZCM00 TANDEM.CIP.H01 005227 CLIM Event CLIM Name: C100271 Logged by CLIM at: Tue Jan 29 15:15:06 2008 kernel: 2008/01/29 23:15:06.912087 stomod: ctd: Table entry 003 deleted

## Slide 15: Using CLIMBKUP/CLIMRSTR
  CLIMBKUP is used to store a copy of the CLIM configuration files in an archive on the NonStop System.
    CIP subsystem configuration is stored in ZSYSCONF database as other modern NonStop SCF subsystems, so that does not need a backup.
    CLIM specific configuration is stored on the CLIMs which are non-fault-tolerant and need a regular backup.
  <TACL> CLIMBKUP n1002531
  The configuration files for CLIM N1002531 would be placed default in $SYSTEM.N1002531.BACKUPGZ, but you can specify another filename.
  Restore the CLIM configuration
    Copies the configuration information from the $SYSTEM disk of the NonStop host system to the CLIM that was saved in the backup operation
    Upon completion of this command, the CLIM must be rebooted to load the new configuration
    Without filename the default filename and location is the same as for CLIMBKUP
<TACL> CLIMRSTR n1002531

## Slide 16: Using the CLIMCMD
  The climcmd is used to execute commands on the CLIMs from a NonStop BladeSystem server
    Use the super user login
  The climcmd is run from a TACL prompt
  Uses the secure shell (with the trust established with SSOCLIM)
  Specific climcmd options are used in place of running the equivalent Debian Linux command
    Never directly edit a CLIM configuration file
  Most Debian Linux command can be executed from the climcmd
    Some commands can not be executed due to terminal requirements
  View the reference (man) pages
Notes: To search for reference (man) pages, user the man –k <string>.
The following command will return all man pages containing the word - clim. <TACL> climcmd <clim-name> man –k clim

## Slide 17: CLIMCMD commands
<TACL> climcmd s1002531 man -k clim
clim (1) - operate, maintain, and assimilate debugging information of the CLIM software
climconfig (1) - configure network protocol parameters
climconfig.arp (1) [arp] - manage arp entries
climconfig.bondmode (1) [bondmode] - change bonding mode, get bondmode info
climconfig.failover (1) [failover] - configure failover
climconfig.hostname (1) [hostname] - manage the CLIM host name
climconfig.interface (1) [interface] - manage CLIM interfaces
climconfig.ip (1) [ip] - add or delete IP addresses
climconfig.psk (1) [psk] - configure pre-shared keys
climconfig.remote (1) [remote] - manage remote configuration for security associations
climconfig.route (1) [route] - configure routes
climconfig.sa (1) [sa] - configure security associations
climconfig.slaveinterface (1) [slaveinterface] - configure bonding interfaces
climconfig.snmp (1) [snmp] - configure snmp
climconfig.sp (1) [sp] - configure security policies
climconfig.sysctl (1) [sysctl] - set or display CLIM kernel parameters
climconfig.tunnel (1) [tunnel] - modify tunnel configuration
climconfig.vpn (1) [vpn] - obtain information about virtual private networks
climstatus (1) - displays CLIM specific status information
hostname (1) - manage the CLIM host name
interface (1) - manage CLIM interfaces
psclim (1) - shows system information about CLIM processes
sysctl (1) - set or display CLIM kernel parameters

## Slide 18: CLIMCMD
<TACL> CLIMCMD {<HOSTNAME> | <IP ADDRESS> | <CLIM NAME>}
  shows all supported Linux commands for the specified CLIM.

## Slide 19: CLIMCMD Examples — List the CLIMs
<TACL> scf info clim $zzcip.*
CIP Info CLIM
Name Mode Location ConnPts Provider
S1002531 STORAGE (100 ,2 ,5 ,3 ,1 ) 2 --
S1002533 STORAGE (100 ,2 ,5 ,3 ,3 ) 2 --
N1002581 IP (100 ,2 ,5 ,8 ,1 ) 1 ZTC0
N1002583 IP (100 ,2 ,5 ,8 ,3 ) 1 ZTC0
Total Errors = 0 Total Warnings = 0

## Slide 20: CLIMCMD Examples — CLIMSTATUS
The climstatus command is a compilation of commands
<TACL> climcmd s1002531 man climstatus
NAME climstatus(1)
climstatus - displays CLIM specific status information
SYNOPSIS climstatus [-o <s,l,r,h,i,f,m,c>]
DESCRIPTION
climstatus is a program that provides the user with CLIM specific status information. The information provided caters to the following objects and/or devices present on the CLIM system: - ServerNet - EtherNet, Local Area Network (LAN) - Kernel IP Routing Table - Secondary Storage Devices, Hard Disk Drives (HDD) - IP Security policies and associations - Interface Failover configuration - SNMP Configuration information - CLIM specific configuration information
Notes: The climstatus command provides status information for all the above mentioned components by default. However, a user can supply an option and choose to view status information pertaining to a particular component.
Options (-o)
s — Displays the status information pertaining to ServerNet
l — Displays the status information pertaining to Local Area Network (EtherNet)
r — Displays the status information pertaining to Kernel IP Routing Table
h —Displays the information pertaining to the file system and disk space usage on the CLIM
i — Displays the information pertaining to the IPSec configuration, and information specific to the IPSec, such as security policies and associations
f — Displays the interface failover configuration
m — Displays the CLIM SNMP Configuration
c —Displays the CLIM specific configuration

## Slide 21: CLIMCMD Examples — CLIMSTATUS (1 of 6)
<TACL> climcmd s1002531 climstatus
CLIM Configuration & Status: Mode.................. STORAGE State................. STARTED ConnPts............... 2 X1 Location........... Group 100, Module 2, Slot 5, Port 3, Fiber 1 Y1 Location........... Group 100, Module 3, Slot 7, Port 3, Fiber 1 X2 Location........... Group 100, Module 2, Slot 5, Port 3, Fiber 2 Y2 Location........... Group 100, Module 3, Slot 7, Port 3, Fiber 2 X1 Connection Status..... UP Y1 Connection Status..... UP X2 Connection Status..... UP Y2 Connection Status..... UP Last Restart Time........ Thu Sep 4 21:17:31 2008 CIP/Linux Hostname....... S1002531 Network SW Version....... T0691H01_01AUG2008_AAB_CLIM Storage SW Version....... T0830H01_01AUG2008_23JUL2008_AAA CIP SW Version........... T0853H01_01AUG2008_23JUL2008_AAA Number of Socket Servers. 1
CIP/Linux Version:Linux version 2.6.18-6-clim-amd64 (Debian 2.6.18.dfsg.1-18hpdeetch1hpde1.9) (brian.haley@hp.com) (gcc version 4.1.2 20061115 (prerelease) (Debian 4.1.1-21)) #1

## Slide 22: CLIMCMD Examples — CLIMSTATUS (2 of 6)
<TACL> climcmd s1002531 climstatus (continued)
SMP PREEMPT Wed Jul 9 21:42:14 UTC 2008 --------------------------------------------------------------Maintenance LAN Status & IP Addresses: Name Status LkP Master / IP Family & Address eth0 UP UP IPv4: 192.168.37.31 IPv6: fe80::21e:bff:fe78:57e Maintenance Provider Interface Status & IP Addresses: Name Status LkP Master / IP Family & Address Other LAN Status & IP Addresses: Name Status LkP Master / IP Family & Address lo UP -- IPv4: 127.0.0.1 IPv6: ::1 sit0 DOWN -- eth1 DOWN DOWN bond0 DOWN DOWN bond1 DOWN DOWN

## Slide 23: CLIMCMD Examples — CLIMSTATUS (3 of 6)
<TACL> climcmd s1002531 climstatus (continued)
Kernel IP routing table
Destination Gateway Genmask Iface
192.168.0.0 * 255.255.0.0 eth0
default 192.168.37.1 0.0.0.0 eth0
---------------------------------------------------------------------
Kernel IPv6 routing table
Destination Next_Hop
Flags Metric Ref Use Iface
::1/128 ::
U 0 244 1 lo fe80::21e:bff:fe78:57e/128 ::
U 0 0 1 lo fe80::/64 ::
U 256 0 0 eth0 ff00::/8 ::
U 256 0 0 eth0

## Slide 24: CLIMCMD Examples — CLIMSTATUS (4 of 6)
<TACL> climcmd s1002531 climstatus (continued)
Filesystem Disk Space Usage
Filesystem Type Size Used Avail Use% Mounted
/dev/sda1 ext3 65G 2.4G 59G 4% /
tmpfs tmpfs 1.7G 0 1.7G 0% /lib/init/rw
udev tmpfs 10M 228K 9.8M 3% /dev
tmpfs tmpfs 1.7G 84K 1.7G 1% /dev/shm

## Slide 25: CLIMCMD Examples — CLIMSTATUS (5 of 6)
<TACL> climcmd s1002531 climstatus (continued)
IPSEC Configuration: Security Policies from SPD (Security policy database): (per-socket policy) in none created: Sep 4 21:16:34 2008 lastused: lifetime: 0(s) validtime: 0(s) spid=99 seq=7 pid=15591 refcnt=1 (per-socket policy) in none created: Sep 4 21:16:34 2008 lastused: lifetime: 0(s) validtime: 0(s) spid=83 seq=6 pid=15591 refcnt=1 (per-socket policy) in none created: Sep 4 21:16:34 2008 lastused: lifetime: 0(s) validtime: 0(s) spid=67 seq=5 pid=15591 refcnt=1
Notes: Continuation of output from the above slide.
(per-socket policy)
in none
created: Sep 4 21:16:34 2008 lastused:
lifetime: 0(s) validtime: 0(s)
spid=51 seq=4 pid=15591
refcnt=1
(per-socket policy)
out none
created: Sep 4 21:16:34 2008 lastused:
lifetime: 0(s) validtime: 0(s)
spid=108 seq=3 pid=15591
refcnt=1
(per-socket policy)
out none
created: Sep 4 21:16:34 2008 lastused:
lifetime: 0(s) validtime: 0(s)
spid=92 seq=2 pid=15591
refcnt=1
(per-socket policy)
out none
created: Sep 4 21:16:34 2008 lastused:
lifetime: 0(s) validtime: 0(s)
spid=76 seq=1 pid=15591
refcnt=1
(per-socket policy)
out none
created: Sep 4 21:16:34 2008 lastused:
lifetime: 0(s) validtime: 0(s)
spid=60 seq=0 pid=15591
refcnt=1

## Slide 26: CLIMCMD Examples — CLIMSTATUS (6 of 6)
<TACL> climcmd s1002531 climstatus (continued)
Security Associations from SAD (Security association database): No SAD entries. --------------------------------------------------------------------- Interface Failover Configuration: None of the failover configuration exists.
--------------------------------------------------------------------- SNMP Configuration: Trap Receiver IP Address 192.168.36.10 192.168.36.11 SNMP Agent State STARTED SNMP Agent Listening IP Address 192.168.37.31 --------------------------------------------------------------------- CLIMPREP Configuration: VERSION 2 CONNECTED_GMS 100.2.5.3.1 SYS_NAME SABER SNET_SPEED 3 NETWORK_CLIM 0 DISK_CLIM 1 OPEN_CLIM 0 SS7_CLIM 0 NUM_SNET_CONN 2 SWITCH_TYPE 3 PCI_SLOTS 1.EM,2.EM,3.DC,4.VO,5.VO

## Slide 27: CLIMCMD Examples — CLIM Processes
Two commands to display CLIM process information
<TACL> climcmd n1002581 psclim
PID RSS %MEM %CPU TIME START STAT CMD
5517 796 0.0 0.0 00:00:00 Sep 4 Ssl /usr/local/bin/climmon --time 0
5565 872 0.0 0.0 00:00:01 Sep 4 Sl confsync
5566 19380 0.4 0.0 00:02:15 Sep 4 Sl cipssrv --number 0
5567 9236 0.2 0.0 00:04:01 Sep 4 Sl climagt --number 1
Termination Info: 0
<TACL> climcmd n1002581 clim status
PID RSS %MEM %CPU TIME START STAT CMD
5517 796 0.0 0.0 00:00:00 Sep 4 Ssl /usr/local/bin/climmon --time 0
5565 872 0.0 0.0 00:00:01 Sep 4 Sl confsync
5566 19380 0.4 0.0 00:02:15 Sep 4 Sl cipssrv --number 0
5567 9236 0.2 0.0 00:04:01 Sep 4 Sl climagt --number 1
Notes: PID — Process ID
RSS — Resident set size of process, the actual amount of memory allocated
STAT — Process state code, (Sleeping, Runnable/Running, Low priority (N), Zombie (defunct), session leader, Multi-threaded (l), Waiting)

## Slide 28: CLIMCMD Examples — Linux Commands (1 of 4)
Execute Debian Linux commands
<TACL> climcmd n1002581 netstat -i
Kernel Interface table
Iface MTU Met RX-OK RX-ERR RX-DRP RX-OVR TX-OK TX-ERR TX-DRP TX-OVR Flg
eth0 1500 0 4430952 0 0 0 2619952 0 0 0 BMRU
eth0: 1500 0 - no statistics available - BMRU
eth1 1500 0 8384055 0 0 0 15877 0 0 0 BMRU
lo 16436 0 816837 0 0 0 816837 0 0 0 LRU

## Slide 29: CLIMCMD Examples — Linux Commands (2 of 4)
<TACL> climcmd n1002581 ls -al /etc
total 872
drwxr-xr-x 54 root root 4096 2008-09-04 19:19 .
drwxr-xr-x 22 root root 4096 2008-08-29 00:00 ..
drwxr-xr-x 3 root root 4096 2008-08-28 23:42 acpi
-rw-r--r-- 1 user root 9832 2008-02-28 22:27 adapters.properties
-rw-r--r-- 1 root root 2803 2008-03-14 15:33 adduser.conf
-rw-r--r-- 1 root root 45 2008-09-04 19:16 adjtime
drwxr-xr-x 2 root root 4096 2008-09-04 17:59 alternatives
drwxr-xr-x 4 root root 4096 2008-08-28 23:42 apt
-rwxr-xr-x 1 root root 4673 2008-07-22 17:27 backup.conf

## Slide 30: CLIMCMD Examples — Linux Commands (3 of 4)
<TACL> climcmd n1002581 ps
PID TTY TIME CMD
1 ? 00:00:00 init
2 ? 00:00:00 migration/0
3 ? 00:00:00 ksoftirqd/0
4 ? 00:00:00 watchdog/0
5 ? 00:00:00 migration/1
6 ? 00:00:00 ksoftirqd/1
7 ? 00:00:00 watchdog/1
8 ? 00:00:00 events/0
9 ? 00:00:00 events/1

## Slide 31: CLIMCMD Examples — Linux Commands (4 of 4)
<TACL> climcmd n1002581 free -m
total used free shared buffers cached
Mem: 3821 387 3434 0 145 77
-/+ buffers/cache: 164 3656
Swap: 2894 0 2894
<TACL> climcmd n1002581 top -n1
TERM environment variable not set.
<TACL> climcmd n1002581 who
16:34:13 up 20 days, 21:16, 0 users, load average: 0.16, 0.04, 0.01
USER TTY FROM LOGIN@ IDLE JCPU PCPU WHAT

## Slide 32: CLIMCMD Examples — CLIMCONFIG
The climconfig command reference (man) page
climconfig - configure network protocol parameters
SYNOPSIS
climcmd hostname|clim-name|ip-address climconfig command [parameter]
DESCRIPTION This command is a parameter to the climcmd command-line interface. It allows you to configure network, IPSec, failover and SNMP parameters.
Enter climcmd at the TACL prompt on the NonStop system followed by the clim-name, CLIM hostname or CLIM IP address, climconfig and one or more command objects and associated parameters.
EXAMPLES
>climcmd 17.24.17.5 climconfig arp -add eth1 -host 17.24.17.50 -hw
address 00:0E:7f:F5:6E:8A

## Slide 33: climconfig man pages
The climconfig command is discussed in a later module.
For details about the climconfig command arguments, see the following reference (man) pages:
  climcmd hostname|clim-name|ip-address man climconfig.arp
  climcmd hostname|clim-name|ip-address man climconfig.bondmode
  climcmd hostname|clim-name|ip-address man climconfig.failover
  climcmd hostname|clim-name|ip-address man climconfig.hostname
  climcmd hostname|clim-name|ip-address man climconfig.interface
  climcmd hostname|clim-name|ip-address man climconfig.ip
  climcmd hostname|clim-name|ip-address man climconfig.psk
  climcmd hostname|clim-name|ip-address man climconfig.remote
  climcmd hostname|clim-name|ip-address man climconfig.route
  climcmd hostname|clim-name|ip-address man climconfig.sa
  climcmd hostname|clim-name|ip-address man climconfig.slaveinterface
  climcmd hostname|clim-name|ip-address man climconfig.snmp
  climcmd hostname|clim-name|ip-address man climconfig.sp
  climcmd hostname|clim-name|ip-address man climconfig.sysctl
  climcmd hostname|clim-name|ip-address man climconfig.tunnel
  climcmd hostname|clim-name|ip-address man climconfig.vpn

## Slide 34
Notes: <footer>
<header>
<date/time>