## Slide 1: IP Cluster I/O Module (CLIM)
Module 4

## Slide 2: Module Objectives
  Introduce the IP Cluster I/O Module (CLIM)
  Describe the hardware components of the IP CLIM
  Describe the IP CLIM theory of operation
  Describe how the IP CLIM connects into the NonStop System
Notes: <footer>
<header>
<date/time>

## Slide 3: Key benefits
State-of-the-art network interconnect:
  Gigabit Ethernet Copper and Fiber NICs
  Future, all new Ethernet NIC easily supported like 10 GB Ethernet
Wealth of IP stack support:
  TCP/IPv4
  TCP/IPv6
  IPSec
  SCTP (Stream Control Transmission Protocol) – Telco specific
Offloads approximately ~30% of TCP/IP load from NonStop CPU to CLIM CPU
Lower system entry cost
Offers 5 x 1 Gb/s interfaces per IP CLIM opposed to 2 x 1 Gb/s and 2 x 100 Mb/s in G4SA

## Slide 4: Choice: IOAME/VIO vs. IP CLIM
IOAME/VIO/G4SA may be the right choice when
  Full failover support is required, with no loss of outside world connections
  Large number of TCPIP stacks are required.
    Capability to run 64 Library copies or TCP/IP stacks and 16+ Conventional TCP/IP stacks. (VIO less)
  Remote Sockets are required (over Expand on other NonStop system)
  Fault Tolerant Sockets are required (only with Conventional TCP/IP)
  TCP/IP over x.25 is required
  SNA over Ethernet is required
IP CLIM may be the right choice when
  High density of Gigabit ports are required
  IP Security or SCTP is required
  When one TCP/IP stack/CLIM or LNP architecture is sufficient
  VLAN or Firewall support is required (planned)
  Bonding failover support is required
  Future communications protocols or options supported by Linux is required
    E.g., enhanced support for mobile devices

## Slide 5: IP Cluster I/O Modules (CLIMs)
P Switches
Ethernet
Storage
SWAN2
ServerNet X Fabric
Storage
CLIM
Storage
CLIM
IP CLIMs
IOAME
Notes: <footer>
<header>
<date/time>
IP CLIMs are also referred to as Network CLIMs.

## Slide 6: IP CLIM Product Overview
The IP Cluster I/O Module (CLIM) is a new generation of Gigabit Ethernet adapters
  HP ProLiant DL385 G5 rackmount server
    Quad core processor
    Debian Linux operating system
  HP standard Gigabit network interface cards
  Redundant ServerNet 3 links
    Supports two X-fabric and two Y-fabric links
  Two IP CLIM products
    Five copper ports
    Three copper ports and two fiber ports
One 72GB system disk
DVD drive not installed
Notes:   The default configuration for an IP CLIM is one X and one Y ServerNet link.
  The HP ProLiant DL385 G2 uses a dual core processor.

## Slide 7: IP CLIM Hardware Overview
  ProLiant DL385 G5 rack mount server
    AMD Opteron, quad core, 2.1GHz processor
    4x1GB PC2-5300 DIMM
    Five PCIe slots
    Redundant power and cooling
  ServerNet 3 to PCI adapter
      Two X-fabric and two Y-fabric connections
  SAS PCI-e HBA (HP SC44Ge)
    Supports Debian OS disk
  Network interface controller (NIC)
    HP NC364T – 4P copper
    HP NC360T – 2P copper
    HP NC373F – 1P fiber
NC364T
NC360T
NC373F

## Slide 8: IP CLIM (Option-A) Ethernet Port Assignments
  Slot 1 is populated with the HP NC364T NIC (4P copper)
  The fifth port is the embedded ETH1 port
  Slots 2 and 4 are empty
Slot 2
3
X4
3
X4
3
X8
4
X8
4
X16
4
133
5
X8
5
133
PCIe
MHz
MHz
PCIe
PCIe
PCI-X
2
X4
PCIe
PCIe
1
X4
UID
2
1
iLO2
iLO
OSM Interface
port
ServerNet Adapter
OSM
Interface port (ETH0 & ETH0:0)
SAS HBA
Slot 3
Slot 5
Slot 4
ETH2
ETH3
ETH4
ETH5
Slot 1
Customer-usable Interface (ETH1)
Notes:   Integrated lights out (iLO) port
  Open system management (OSM)

## Slide 9: IP CLIM (Option-B) Ethernet Port Assignments
  Slot 1 is populated with the HP NC360T NIC (2P copper)
  Slots 2 and 4 are populated with the HP NC373F NIC (1P fiber)
  The fifth port is the embedded ETH1 port
3
X4
3
X4
3
X8
4
X8
4
X16
4
133
5
X8
5
133
PCIe
MHz
MHz
PCIe
PCIe
PCI-X
2
X4
PCIe
PCIe
1
X4
UID
2
1
iLO2
SAS HBA
Slot 2
Slot 1
iLO
ServerNet Adapter
OSM (ETH0:0)
Interface port
Slot 3
Slot 5
Slot 4
ETH1
ETH3
ETH2
ETH5
ETH4

## Slide 10: IP CLIM Adapters
  The IP CLIM can replace the IOAME/G4SA
    Gigabit Ethernet connectivity: copper/fiber ports
    TCP/IP v4
    TCP/IP v6
    Internet Protocol Security (IPsec)
  ProLiant server running Debian Linux
    PCI-e cards for ServerNet connection
    Uses Linux device driver(s) to transfer data to the Ethernet NIC cards
    Does not allow any customer code or applications
    Linux “personality” is hidden
  Offloads approximately 30 percent of the TCP/IP load from a NonStop CPU to a CLIM CPU
Notes: <footer>
<header>
<date/time>

## Slide 11: Theory of Operation
  Cluster I/O Protocol (CIP) Subsystem
    Provides a configuration and management interface for I/O
  Uses a Linux server as a front end
    Moves network stacks from the NonStop host to a Linux server
  Leverages the open source Linux environment
  Provides support for IPsec, SCTP, IPv6
  Dual ServerNet fabrics connections
  Provides Gigabit Ethernet interfaces
  The IP CLIM provides the physical interface to the network
NonStop NS-2000
Application
Socket Calls
IP CLIM SW
TCP Stack
IP CLIM SW
Ethernet Links
ServerNet
IP CLIM
Notes: Internet Protocol Security (IPsec) — Suite of protocols for securing IP communications by authenticating and/or encrypting the IP packets. No application design changes are needed for IPsec.
Stream Control Transmission Protocol (SCTP) — Uses a simpler basic packet structure than TCP or UDP
Internet [protocol version 6 (IPv6) — Successor to IPv4. IPv6 uses larger address space than IPv4.

## Slide 12: IP CLIM — Recommended FRUs
FRUs | Online replaceable? | Hot-Pluggable?
Microprocessor | No | No
Memory | No | No
Power supply | Yes | Yes
Fan | Yes | Yes
PCI-e Riser | No | No
4P copper NIC | No | No
2P copper NIC | No | No
1P fiber NIC | No | No
ServerNet dapter | No | No
Debian OS disk | No | Yes

## Slide 13: IP CLIM Failover
Two types of failover
  Intra-CLIM failover
    Bonds two or more, physical interfaces
      Uses an Active-backup policy
    Failover is seamless, no loss of TCP connections
  CLIM to CLIM failover
    CIPMAN moves the interface from a failing CLIM to the failover CLIM
    TCP connections are lost
      A reset is issued
    Listening and UDP sockets survive

## Slide 14
Notes: <footer>
<header>
<date/time>