## Slide 1: New NonStop Hardware Architecture Overview (with CLIMs)
Module 2

## Slide 2: Module Objectives
  Architecture Overview of HP Integrity NonStop Servers and HP NonStop BladeSystems using CLIMs
  Overview of HP Integrity NS16x00 with CLIMs
  Overview of HP Integrity NS2000 with CLIMs
  Overview of HP NonStop BladeSystems NB50000 with CLIMs
  Describe the basic functions of the CLIMs
Notes: <footer>
<header>
<date/time>

## Slide 3: General NonStop system architecture
ServerNet Switches
ServerNet Interconnect
Integrity NonStop System Processors (Single or Multicore)
Network Adapter
SWAN
I/O Adapters
Storage Adapter
Peripherals
Storage Adapter
Network Adapter
Storage

## Slide 4: NonStop system architecture with IOAME or VIO (NS1x00)
ServerNet Switches
ServerNet Interconnect
Integrity NonStop System Processors (Single or Multicore)
G4SA
SWAN
I/O Adapters
FCSA
Peripherals
FCSA
G4SA
FC Storage

## Slide 5: NonStop system architecture with CLIMs
ServerNet Switches
ServerNet Interconnect
Integrity NonStop System Processors (Single or Multicore)
IP CLIM
SWAN
I/O Adapters
Storage CLIM
Peripherals
Storage CLIM
IP CLIM
SAS/FC Storage
Notes: FC Storage supported on the CLIMs

## Slide 6: Why CLIMs?
IOAME/VIO/FCSA/G4SA
  Proprietary Hardware
  Proprietary Software (embedded on adapter)
  For every new protocol for Storage and Networking, new interface technology and software needs to be developed by the NonStop Enterprise Division.
IP and Network CLIM
  Open Standards Hardware
  Open Standards Software (Debian Linux Operating system including I/O stacks)
  Can deploy new software and hardware technologies very easily
  NonStop Enterprise Division needs only to develop/maintain interface hardware/software between NonStop OS and CLIMs.

## Slide 7: System Comparison — Hardware
 | NS Blades | NS16200 | NS2000
Architecture | NSMA | NSAA | NSMA
Processor module | bl860c blade | rx4640-NED 5U slice | rx2660 2U server
Processor redundancy | No | Yes, through LSU | No
Multicore architecture | Yes, 2-way | No | Yes, 2-way
Logical CPUs per node | 2 to 16 | 2 to 16 | 2 or 4
Memory per CPU | 8 to 48 GB | 4, 8 or 16 GB | 8 or 16 GB
ServerNet switch | HP ServerNet SWM | P-Switch module | VIO module
IO infrastructure | CLIM, IOAME | IOAM, CLIM | VIO module, CLIM (No FCSA in VIO)
Storage options | MSA70, FC tape, XP, SAS tape | FCDM, XP, FC tape | MSA70, XP, FC tape, SAS tape
Cluster support | Yes | Yes | No

## Slide 8: HP NonStop Multicore Architecture (NSMA) With NS2000
<number>
July 28, 2026
CPU 3
Intel Itanium
9100 Series
SNet Interface
Memory
Core 1
Core 0
VIO /ServerNet
CPU 2
Intel Itanium
9100 Series
SNet Interface
Memory
Core 1
Core 0
CPU 1
Intel Itanium
9100 Series
SNet Interface
Memory
Core 1
Core 0
CPU 0
Intel Itanium
9100 Series
SNet Interface
Memory
Core 1
Core 0
Notes: <footer>
<header>
<date/time>

## Slide 9: Common Elements of the NS-2000 Servers
  Two or four NS-2000 blade elements
    Each elements is an HP Integrity rx2660 server with one dual-core 1.42GHz/12MB Montvale processor
    One Capella ServerNet PCI card
  8GB or16GB memory per logical processor
  Two Versatile I/O (VIO) modules for HP NonStop ServerNet interconnectivity and Ethernet connectivity
VIO
CPU 1
CPU 0
VIO

## Slide 10: Overview of the NS-2000 Server
  AC powered
  Two Storage Cluster I/O Modules (CLIMs)
    Two MSA70 Serial Attached SCSI (SAS) disk enclosures
  One Maintenance switch
  One rack-mounted system console
  A 42U or a 36U G2 rack
    1U = 1.75-inch/44.45mm
  Optional
    Telco CLIM (default 0, max 2)
    IP CLIM (default 0, max 2)
    UPS & extended run-time modules (ERMs)
    Virtual tape server (VTS)

## Slide 11: NS-2000 Server Configurations

## Slide 12: HP Integrity NonStop NB50000c BladeSystem Example
An 8p NSMA system uses one 42U rack
  Up to 48GB main memory per logical processor
  48 Cluster I/O Modules (CLIMs) per 16p system
  Five Gigabit Ethernet ports per IP CLIM
  25 SAS disk drives per Disk Enclosure
  (72GB/15K RPM or 146GB/10K RPM)
C7000 Enclosure
IP CLIMs
Storage
CLIMs
SAS Disks
UPS
Maintenance Switch
Notes: <footer>
<header>
<date/time>
  SAS — Serial Attached SCSI
  IOAME — I/O adapter module enclosure
  G4SA — 4port Giga-bit ServerNet adapter
  FCSA — Fibre Channel ServerNet adapter
  FCDM — Fibre Channel disk module
  ERM — Extended run-time module for un-interruptible power supply (UPS)

## Slide 13: HP Integrity NonStop NS16200
Intel Montvale processor at 1.6 GHz with 12 MB cache
1.2 X performance over NS16000
Triple- (TMR) and Dual- (DMR) Modular Redundancy
Linear scalability :
  2–16 processors per node
  4–16 GB memory per processor
  Support clustering up to 4,080 processors
Industry Standard Connections (IOAME)
  60 I/O adapters
  Fibre Channel disk storage (FCDM and SAN XP)
  Gigabit Ethernet
Connects to HP NonStop S-series disk and I/O
Now supports CLIMs as well
Delivers highest service levels for most demanding applications
Notes: <footer>
<header>
<date/time>

## Slide 14: Modular Fabric Topology
P-Switch
(X Fabric)
P-Switch
(Y Fabric)
CLIM
IOAME
IOAME
CLIM
IOAME
X Fabric
Y Fabric
Adapter
Adapter
IOAME
Maximum of 10
ServerNet Adapters per IOAME
Blade Element
Blade Element
Cluster Switch
(X Fabric)
Cluster Switch
(Y Fabric)
Blade Element
LSUs
Notes: <footer>
<header>
<date/time>
System Fabric
  Centralized versus distributed fabric as in the NonStop S-series
  All fiber interconnect
    Cable management considerations
Ethernet Maintenance Fabric
  Connects the maintenance entities on all ServerNet switch board P-switches and system consoles.
  Dual maintenance switches and dual consoles are recommended.
  Switch configuration mirrors that of the ServerNet fabric.

## Slide 15: NonStop BladeSystem
P Switches
Ethernet
Storage
ServerNet
SWAN
Storage CLIM
Storage CLIM
IP CLIM
IP CLIM
SWAN2
2-16 NonStop Processors
IOAME
Notes: <footer>
<header>
<date/time>

## Slide 16: HP Integrity NonStop NB50000c BladeSystem
  The highest performance per CPU of the NonStop Servers
  ServerNet 3 based
    Clusters with the Integrity NonStop NS-series and S-series systems that support clustering
  Not NonStop advanced architecture (NSAA) based
    The fault zone is the blade==CPU
      When one IPU fails the CPU fails
    The same fault model as the NonStop S-series and NonStop value architecture (NSVA)
  Uses Cluster I/O Modules (CLIM)
    Storage CLIM
    IP CLIM (also referred to as a Network CLIM)
  Supports IOAME (FCSA, G4SA)

## Slide 17: NonStop Server Blades — Logical System View
Four Logical Processors
1 board == 1 CPU
2 cores == 1 chip (socket)
Switch - Y
ServerNet
Switch - X
CPU 0
core
0
core
1
Memory
SNet Interface
CPU 1
core
0
core
1
Memory
SNet Interface
CPU 2
core
0
core
1
Memory
SNet Interface
CPU 3
core
0
core
1
Memory
SNet Interface
Montvale Chip
NonStop BL860c server blade with 1p/2c = 1 logical processor
Notes: <footer>
<header>
<date/time>
  This above slide shows a four-CPU view with cores.

## Slide 18: NB50000c Configurations
  The HP Integrity NonStop BL860c Server Blade is a full height server blade
    Eight server blades (8P) per enclosure
  Forty-eight ServerNet I/O links per fabric per 16P system
      Maximum of 6 x4 optical ports per ServerNet switch module (SWM) for IO => 24 links per 8P
    Current limit of 24 CLIMs per 16P system (software)
      The Storage CLIM uses two ServerNet links for disk performance
      The IP CLIM is configurable for either one or two links (performance versus connectivity)
    Support for six IOAME modules per 16P system
      Requires x4 fat pipe so there are only four IOAMEs per 8P chassis
Notes: <footer>
<header>
<date/time>
  Cluster connectivity
    Twenty-two ServerNet links for MESH style interconnect (x4 optical ports)
    Two ServerNet links for supercluster connections (SFPs)

## Slide 19: Theory of Operation — HP BladeSystem c7000 Enclosure
  Provides high performance computing engines for HP NonStop systems
  Provides environmental monitoring services to the Onboard Administrator (OA)
  HP Insight display
  Uses a PCI Express x4 connection to the ServerNet host bus adapter (HBA)
  Six power supplies that support Dynamic Power Saving Mode

## Slide 20: c7000 Enclosure Configuration
PSU
PSU
PSU
PSU
PSU
PSU
BL860c
BL860c
BL860c
BL860c
AC input module
FAN
FAN
FAN
FAN
FAN
FAN
FAN
FAN
FAN
FAN
OA
GbE
GbE
ServerNet Switch - X
ServerNet Switch - Y
OA
Front
Rear
Switch Modules
Server Blades
BL860c
BL860c
BL860c
BL860c
Empty
Empty
Notes:   HP BladeSystem Onboard Administrator (OA)
  Power supply unit (PSU)
  Gigabit Ethernet (GbE)

## Slide 21: C7000 Enclosure
  Active cool fans
    Redundant fan design
  Interconnect bays
    Four redundant interconnect fabrics
    Redundant connections to each server blade
  Onboard Administrators and midplane
    Redundant active/passive design
    Midplane fully redundant
      No active components
    Both OAs can fail causing no effect to the system
  Power management
    Redundant AC
      3 + 3 power supplies
    No fault zones
    Three power supplies sustain enclosure
Rear View
Notes: <footer>
<header>
<date/time>

## Slide 22
Notes: <footer>
<header>
<date/time>